## Slide 1
Emerging and Proven Waste Conversion Technologies for the 21st Century
Paul Hauck, P.E.
CDM Smith
1715 N. Westshore Boulevard Suite 875
Tampa, Florida 33607
(813) 281-2900
hauckpl@cdmsmith.com
City of Jacksonville
Solid Waste Workshop
November 29, 2012

## Slide 2: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 3: Solid Waste Services
Waste-to-Energy
Transfer stations
Material recovery facilities
Landfills
Rate/financial studies
Recycling

## Slide 4: CDM Smith Waste-to-Energy Experience
Introduction

## Slide 5
CDM Smith Florida Solid Waste Experience
Introduction

## Slide 6: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 7: City of Jacksonville Current Disposal Summary
Landfill Operator
Leachate Collection & Disposal
Third Party Methane Collection & Energy Generation
Materials Recovery Facility
Yard Waste Processing Facility
48%
Notes: Transition from transport to disposal. Add MRF and yard recycling to flowchart.
Class I – TRL (Class I, Class III, and Commercial MSW )
- operation
- COJ collects tipping fee (COJ staff)
- WM/Operator places waste on the fill (WM paid as operator)
- methane gas pulled off of the hill (third party agreement PPP)
- leachate collection goes to JEA
Class III – goes to TRL
C&D disposal facilities – TRL, Ottis Rd, Jones Rd, Old Kings Rd

## Slide 8: Duval County Landfill Current Status
Approximately 22% of airspace remaining
Phase 1-5 build-out anticipated January 2018
  Population growth
  No hurricane debris
  Settlement/density
To meet Phase 1-5 build-out, construction of Phase 6 completed by July 2016
  + 6 month selective placement of waste
  + 1 year general contingency

## Slide 10: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 11: The Future of Waste Management
Emerging Paradigms

## Slide 12: Waste Conversion By-Products Continue to Grow in Economic Value
Conversion Technology | Power |  | Fuels / Chemicals |  |  |  | Amendments/ Aggregates | 
 | Steam / Heat | Electric | Syn Gas | Bio Methane | Chemical | Fuels | Aggregate | Mulch / Compost
Thermal |  |  |  |  |  |  |  | 
Biological / Chemical |  |  |  |  |  |  |  | 
Physical |  |  |  |  |  |  |  | 
Emerging Paradigms
Notes: Reduce words , add graphics

## Slide 13: Cost and Affordability
Criteria Description | Solid Waste Alternatives |  |  | 
 | Landfill (Phase 6A & 6B) | Massburn WTE | Waste to Biofuels | Thermal Gasification WTE
Market Readiness | Now | Now | 5-10 years | 10-15 years
Capital Cost |  |  |  | 
Year 2013 | $43M | $400M | $500M | $300 M- $500 M
Operational Cost--Unit Cost/ton |  |  |  | 
Potential Revenue is Not Included in O&M Cost for the Various Options | $18.10/ton | $35/ton | $45-$50/ton | $30/ton-$45/ton

## Slide 14: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 15: Modern Waste-to-Energy (WTE)
WTE disposes of 13% of the nation’s waste (U.S. EPA)
  86 operating facilities
  36 million people served
  27 states
  Generation capacity in excess of 2,700 MW
  16 million MWhrs of renewable power generated annually
  259 million tons per year currently disposed of in landfills represents an additional 142,450,000 MWhrs annually (equivalent to 16,261 MW of capacity)
Proven Waste Conversion Technologies
Notes: Note: Last bullet may not be as applicable to TRL, need to discuss how to present this one

## Slide 16: Dominant WTE Technology in U.S. …Advanced Massburn Combustion
Technology Types
  ~ 74% are massburn facilities
  ~ 14% are refuse-derived fuel (RDF) facilities
  ~ 9% are modular
Energy Production
  73% produce only electricity
  20% produce steam and electricity
  7% produce steam only
Proven Waste Conversion Technologies
Massburn requires no pre-processing of MSW

## Slide 17: WTE Ownership and Operation in the U.S.
Ownership
  52% Privately Owned
  48% Publically Owned
Operation and Management
  84% Privately Operated
  16% Publically Operated
Proven Waste Conversion Technologies

## Slide 18
PILOT SCALE | DEMONSTRATION | MARKET ENTRY | MARKET PENETRATION | MARKET MATURITY
Stoker
Co-firing
(utility boilers)
Fluidized Bed
Small Gasifier/
IC Engine
Gasification – Boilers, Kilns
Pyrolysis and Depolymerization
Other Conversion Processes 1
Massburn WTE & RDF Combustion2
Biomass Direct Combustion
Biomass Gasification & Pyrolysis
Waste-to- Energy
Includes RDF gasification, plasma gasification, and pyrolysis
RDF = Refuse-derived fuel
EMERGING (Higher Risk)
PROVEN (Lower Risk)
STATE
of
TECHNOLOGY
Co- Digestion
Anaerobic Digestion/ Ethanol
Emerging Waste Conversion Technologies

## Slide 19: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
  Proven: Massburn, Ethanol
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 20: Florida Waste-to-Energy Facilities 12 Facilities – 607 MW of Renewable Electricity
Proven Waste Conversion Technologies

## Slide 21: Typical Massburn WTE Crosssectional Diagram
Notes: Slide 27 or 28, not both

## Slide 22: Continuous Reductions of Emissions from Large and Small Municipal Waste Combustors
Proven Waste Conversion Technologies
Pollutant | 1990 Emissions (TPY) | 2005 Emissions (TPY) | Percent Reduction
CDD/CDF TEQ Basis * | 44 | 15 | 99+%
Mercury | 57 | 2.3 | 96%
Cadmium | 9.6 | 0.4 | 96%
Lead | 170 | 5.5 | 97%
Particulate Matter | 18,600 | 780 | 96%
HCL | 57,400 | 3,200 | 94%
SO2 | 38,300 | 4,600 | 88%
NOx | 64,900 | 49,500 | 24%
Source: EPA, August 2007
* Dioxin/furan emissions are in units of grams per year toxic equivalent quantity (TEQ), using
1989 NATO toxicity factors; all other pollutant emissions are in units of tons per year

## Slide 23: Refuse Storage Pit at Massburn WTE Facility
Proven Waste Conversion Technologies
Modern WTE facilities typically store 5 – 7 days of MSW

## Slide 24: Advantages of Massburn WTE… Minimal Residuals to the Landfill
Typical WTE Ash Residue
75% weight reduction
90% volume reduction
Proven Waste Conversion Technologies

## Slide 25: Metals Liberated by the Combustion Process Recovered and Recycled for Additional Revenues
Ferrous metals everything…including the kitchen sink
Non-ferrous metals (aluminum, brass, bronze, copper, gold, silver, stainless)
Proven Waste Conversion Technologies

## Slide 26
Ethanol Production from Urban Yard and Wood Waste
Promising Waste Conversion Technologies
Future Feedstock for Cellulosic Ethanol: 10 MGY facility will require ~200,000 tons per year
Notes: How much yard waste does COJ produce? Put in context of 200 kton/yr

## Slide 27
PILOT SCALE | DEMONSTRATION | MARKET ENTRY | MARKET PENETRATION | MARKET MATURITY
Stoker
Co-firing
(utility boilers)
Fluidized Bed
Small Gasifier/
IC Engine
Gasification – Boilers, Kilns
Pyrolysis and Depolymerization
Other Conversion Processes 1
Massburn WTE & RDF Combustion2
Biomass Direct Combustion
Biomass Gasification & Pyrolysis
Waste-to- Energy
Includes RDF gasification, plasma gasification, and pyrolysis
RDF = Refuse-derived fuel
EMERGING (Higher Risk)
PROVEN (Lower Risk)
STATE
of
TECHNOLOGY
Co- Digestion
Anaerobic Digestion
Emerging Waste Conversion Technologies

## Slide 28: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
  In Development: Plasma Arc Gasification, Staged Combustion
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 29: Reference Plasma Arc Projects
Japan
  Yoshi (Hitachi Metals, 166 TPD pilot plant 1999 to 2000)
  Utashinai City ( 165 TPD in 2002)
  Mihama / Mikata (28 TPD in 2002)
Canada
  Ottawa (100 TPD demonstration scale in 2008)
England
  Faringdon, Oxfordshire (Advanced Plasma Power -modular test facility)
Experimental Waste Conversion Technologies

## Slide 30: St. Lucie County Plasma Gasification Project
6 year development process, project abandoned in 2011
2012 St. Lucie County selected Covanta for CleerGas Process
2 X 300 TPD for Combined Heat and Power
Promising Waste Conversion Technologies

## Slide 31: Current St. Lucie County Covanta Gasification Project
  Better control of syngas combustion – lower NOx and CO generation
  Lower air requirement – lower flue gas flow, higher boiler efficiency, lower particulate, smaller equipment
Promising Waste Conversion Technologies
Performance advantages vs. conventional WTE:

## Slide 32: Florida Recent WTE Success Stories
Indian River County Bio-Energy Center
Palm Beach County 3,000-TPD Massburn Facility

## Slide 33: Ineos Bio-Energy Center (2012) Indian River County Florida
400 direct jobs in construction, engineering and manufacturing
Injected more than $25 million dollars directly into the Florida economy
60 full-time employees
$4 million annually in payroll to the local community
Promising Waste Conversion Technologies
Phase 1: 8MG/yr from 400 tpd biomass
Phase 2: 50MG/yr from MSW/RDF

## Slide 34: Palm Beach County, Florida (2012) New 3,000-TPD Massburn WTE Rendering Incorporating Both Sustainability and Aesthetics
2 MG
Florida Case Studies – Palm Beach County
Notes: Note the high level of aesthetics for the project, along with the focus on sustainability. The existing 2,000 tpd RDF WTE facility is located in the foreground.

## Slide 35: Today’s Presentation
CDM Smith solid waste experience
Current solid waste system
Benefits and Limitations of Waste Conversion Technologies
Waste Conversion Technology Examples
The Long Term – 15 to 20 years in the future
COJ Solid Waste Strategy

## Slide 36: My Vision of the Future of WTE and Industry…
Integration of MRFs with WTE facilities
Recycling of ash with other recycled aggregates (crushed concrete, RAP, ceramics, brick, stone, etc.)
Internal use of renewable electricity for powering of water treatment and recycling processes
Biorefinery projects (waste-to-biofuels) including addition of local energy crops
The paradigm of the 21st century shifts from waste management to “Resource Management”
Conclusion
Notes: Inextricably = Unavoidable; inescapable

## Slide 37: Municipal Utility Campus Synergies
WTE
Solid Waste
WWTP
WTP
Excess Electricity to Grid
Electricity to
Utility Complex
Wells
Potable Water
to Grid
Sanitary Waste
Excess Stormwater
Reclaimed
Water
Wet Weather
Storage
Reclaimed Water to Grid
Integration of waste-to-energy with water and wastewater treatment plants
Synergistic Opportunities – WTE and Water
MRF
Notes: Sample diagram of a future cascading water recycling process

## Slide 38: Landfills…Lowest Rung of the ISWM System, But Prime Sites for Development of Eco-Parks
Reliable supply of feedstock
  MSW, C&D Wastes, Biomass
Proper zoning and buffer
from neighboring developments
Generally have land suitable for development and temporary stockpiling of resources (aggregates, biomass, tires, wood)
LFGTE can also be used for Eco-campus
  Internal use of electricity
  Internal use of biogas for heat (drying of WWTP biosolids)
  Alternate to CNG for powering waste collection fleet
Integrated Solid Waste Management

## Slide 39: Palm Beach County Florida ISWM Campus
Florida Case Studies – Palm Beach County
Notes: The first new WTE facility in the US in the last 16 years has just broken ground in Florida. It will process 3,000 tpd and located on an integrated solid waste management campus, and adjacent to an existing 2,000 tpd RDF WTE facility.

## Slide 40: Palm Beach County, Florida Regional Biosolids Processing Facility
Florida Case Studies – Palm Beach County

## Slide 41: City of Jacksonville Solid Waste Strategy
Permit full landfill expansion
Take advantage of favorable permitting environment
Landfill expansion represents the most impactful land use for permitting purposes
Phase 6-8 Landfill Expansion

## Slide 42: City of Jacksonville Solid Waste Strategy
Options are open to modify the permit to accommodate future WTE technology
City evaluated Massburn in 1984 and decided not to pursue it
Other WTE technologies are not ready for commercial scale implementation
Phase 6 Landfill Expansion
Landfill reserved for WTE byproducts
Future Technology (WTE)

## Slide 43: Thank You for the Opportunity to Share!
Conclusion
Paul Hauck, P.E.
CDM Smith
1715 N. Westshore Boulevard, Suite 875
Tampa, Florida 33607
(813) 281-2900
hauckpl@cdmsmith.com
We’ll see it, when we believe it!

## Slide 44: My Humble Career
BS Mechanical Engineering 1973
Commercial Nuclear Power Industry (17 years)
Waste-to-Energy Industry (23 years)
  Construction
  Research and Marketing
  Consulting (WTE Retrofits, Expansions, O&M)
Public Works Consulting (10 years)
Ethanol Project Development (2 years)
CDM Smith Emerging Waste Conversion Technologies Discipline Leader (5 years)